## Slide 1: Research Summary 2013-14 Academic Year
09 May 2014

## Slide 2: Overview - Pterodactyl
Pterodactyl Project Goals
Project Motivation
Background Research
Vehicle Design
Simulation and Control
  Airplane Mode
  Rotorcraft Mode
Design Optimization
Future Work

## Slide 3: Project Goals
Design and build autonomous aircraft
Morphing design for improved versatility
Quantify performance characteristics
Optimize design geometry

## Slide 4: Project Motivation
A morphing UAS can adapt to its mission
  Operate as plane for covering long distances
  Operate as rotorcraft for landing/loiter
  Potential to use morphing as control surface
Compact design is easily deployable/retrievable
Develop techniques for quantifying performance

## Slide 5: Background Research
Developed 6-DoF simulator
  Good accuracy/speed trade off at 100 Hz
  Can be run at 1 kHz for heightened fidelity
  Implemented for Euler angles and quaternions
NACA 0012 airfoil used for body
  Aerodynamic look-up tables utilized
  Data compiled by Trevor Bennett
  Using Strips theory for lateral/longitudinal coupling

## Slide 6: Vehicle Design

## Slide 7: Vehicle Design
Planform on previous slide is dynamically generated by Matlab
  Angle to leading edge and hinge positions variable
  Green dots represent aerodynamic centers of strips
  The 4 triangular portions are treated as flat plates
Major modification to original design
  Originally to have double coaxial center propeller
  Mechanically simpler to separate them
  Expands the control envelope

## Slide 8: Simulation and Control - Airplane
So far only have lift, drag and pitching moment
  Non-dimensional terms obtained from look-up table
  No control surfaces yet
  Roll, yaw and sideslip accounted for

## Slide 9: Simulation and Control - Rotorcraft
Forces and moments come from the propellers only
Control strategy comes from quadcopters
  Yawing moment comes from rotor torque
  Non-parallel axes provides additional yaw
Inner-loop, outer-loop control
  Outer loop calculates heading
  Inner loop calculates thrust from each propeller
Sensitive to the aircraft model

## Slide 10: Design Optimization

## Slide 11: Future Work
Finalize design
Generate more accurate model of the aircraft
Determine appropriate gains for rotorcraft mode
Design actuators for airplane mode
Develop control system for airplane mode
Construct and test vehicle

## Slide 12: Overview – Dynamic Resource Allocation
Project Goals
Project Motivation
Methods Explored
  Markov Decision Processes
  Distributed Clustering
Preliminary Results

## Slide 13: Project Goals
Develop small, low-cost weapons that cooperate
  Ensure full engagement of all targets
  Avoid wasting weapons
Minimize communication required
  Communication may be unreliable in practice
  A small network may be too sparse

## Slide 14: Project Motivation
Asymmetric conflict scenarios
  Targets easily replaced
  Targets less valuable than weapons used
Scenarios requiring precision
  Targets intermixed with non-targets
  Preferable to avoid unnecessary damage
Alternative applications of techniques
  Selecting patients in a triage situation
  Robots moving furniture

## Slide 15: Markov Decision Processes
MDPs are a planning tool to generate policies
  A policy maps states to one and only one action
  MDPs generate optimal policies
MDPs require observable domains
  List of potential states
  List of possible actions in each states
  State-transitions describe possible action results
  Reward function for results of each action
Extensible to partially observable domains

## Slide 16: Markov Decision Processes
Value Iteration vs Policy Iteration
  Value – policy that maximizes expected reward
  Policy – policy such that no other policy is better
  Policy often converges much faster
MDPs suffer the curse of dimensionality
  Naïve representation
  Adding distance exacerbates the problem
Despite these problems, MDPs are very powerful

## Slide 17: Distributed Clustering
Robots initially select closest target
If that target is over-engaged, chance of switching
  Sigmoid threshold applied to this chance
  New target is chosen randomly
  Probability distribution based on distance
Requires less knowledge than MDP
  Needs distance to each target
  Total number targeting current target
  Knowledge from sensors and local robots only

## Slide 18: Preliminary Results